## Slide 1
MODULE 4
BUSHFIRE BEHAVIOUR IN
THE LANDSCAPE
Notes: Ask students to open up their learning journals and make a title page for Bushfire in Behaviour in Landscape.

## Slide 2
PART 1
THE FIRE TRIANGLE

## Slide 3
THE FIRE TRIANGLE
What three things does a fire need
to burn?
Notes: Ask students to open to a new page in their learning journal and write a heading for the Fire Triangle. Students can draw the draw the diagram on the slide or paste in a printed version. Tell the students to write in the three things that a fire needs to burn (NOTE: Use grey lead pencil in case it needs to be corrected). Invite some of the students to share their answers.

## Slide 4
THE FIRE TRIANGLE
Fire needs fuel, heat and oxygen to burn.
Notes: Present the slide and give the students some time to make any corrections on the diagram.

## Slide 5
Notes: Watch the Mr Wizard video about the Fire Triangle. NOTE: It was not possible to embed the video in the slide- this is only a screen shot.
Link to video: https://www.youtube.com/watch?v=kGGUNM9D78A

## Slide 6
QUIZ TIME!
Notes: Complete the kahoot quiz about the fire triangle (6 Questions)
https://create.kahoot.it/share/the-fire-triangle/97e0e311-c137-4496-8feb-922491876b17
Explanations for each of the quiz answers are provided below:
1. Spraying water on the fire > removes heat > the water cools the fuel down until it's too cool to burn
2. Putting a fire blanket on the fire > removes oxygen – the blanket cuts off the supply of oxygen and puts the fire out.
3. Using a bulldozer to clear the vegetation > removes fuel – the bulldozer is removing all the fuel so the fire has nothing to burn
4. Putting out campfire with a bucket of water > heat > the bucket of water cools the fuel so it can no longer burn.
5. Stop, drop and roll > removes oxygen > rolling on the ground smothers the fire and starves it of oxygen.
6. Burning off leaf litter > removes fuel – when the leaves are already burnt, the fire has nothing to burn.
NOTE: You will find a powerpoint version of this quiz on the website here: https://www.cfa.vic.gov.au/ArticleDocuments/2734/Worksheet%201_Fire%20Triangle%20Quiz.pptx

## Slide 7: Part 2
HOW DO BUSHFIRES START?

## Slide 8
LET’S BRAINSTORM!
HOW DO BUSHFIRES START?
Notes: Get the students to open their learning journals. Make a “Heading how do bushfires start?”
Students can work with a partner to list as many causes as they can think of.
Reconvene the class. Invite students to share their ideas and write them up on the board.
When the students have contributed everything on their lists, ask them “Which cause is the most common in Victoria?”

## Slide 9: THE FOUR MAIN CAUSES OF BUSHFIRES IN VICTORIA
Undetermined
It has not been possible to identify the cause of the fire. The cause of the fire remains unknown.
Suspicious
Fire agencies suspect that the fire has been started deliberately (e.g. arson), but they need to investigate to find out.
Lightning
Lightning strikes the ground and ignites dry vegetation with intense heat. This starts a small fire which turns into a bushfire.
Accidents / negligence
The fire started due to human mistakes or carelessness (e.g. not putting a campfire out properly, sparks from power tools).
Notes: Talk through the information on the slide.
Ask the students to rank the four causes in order from most common to least common. They can do this pairs or individually. When they are finished, invite some of the students to share their rankings.

## Slide 10
Chart: 
Chart: 
| Undetermined | Suspicious | Lightning | Accident/negligence
 | 0.228 | 0.209 | 0.164 | 0.399
Notes: As a class, discuss the data in the pie chart. What is the most common cause? What is the second most common? Third? Fourth? Ask the students to compare their rankings to the data in the pie chart – Which ones did they guess correctly? Which ones did they get wrong?
Facilitate a short discussion about the implications of this data for bushfire safety (e.g. If 40% of bushfires are caused by accidents and negligence, what does that mean for what WE can do to prevent bushfires from starting in the first place?)

## Slide 11: CAMPFIRE SAFETY
Do
Don’t
Notes: Ask the students “Have you ever been camping?” “Have you ever had a camp fire?” “What did you do to ensure your campfire didn’t start a bushfire?”
Put the students in pairs. Instruct them to open a new page in their learning journal and write the heading ‘Campfire Safety’. Underneath, draw a table with two columns and label them ‘Do’ and ‘Don’t’
Tell them they are going to watch a video about campfire safety and they need to record as many dos and don’ts as they can.

## Slide 12
Notes: Play the video once. The students won’t have time to write down all of the dos and don’t because it moves quickly. Tell the students that you are going to play it again and this time they need to tell you when to pause so they can write down the do or don’t. They will need to listen carefully. You may need to play it a couple of times.
When the students think they have recorded all the dos and don’ts, review them against these lists:
Dos
Check if it’s a total fire ban
Set up camp and store supplies 3m away from your camp fire
Build you campfire so it’s no bigger than 1m wide and 1m long
Extinguish your campfire with water
Don’t
Light a campfire if a total fire ban is in place
Leave a burning campfire unattended
Put rubbish or food scraps in your fire
Scrape dirt over the top of your campfire
Leave hot embers in your campfire
Finish this activity with a short class discussion about the role they can play in campfire safety. Prompt: Now that you have this knowledge about campfire safety, what can you do to help prevent bushfires? (e.g. practice good campfire safety themselves, educate others about campfire safety)

## Slide 13: Part 3
HOW DO BUSHFIRES SPREAD?

## Slide 14
A bushfire has started in the National Park. It’s spreading quickly through the landscape.
How is it spreading?
Notes: Facilitate a discussion with students about how this bushfire is spreading.

## Slide 15
BUSHFIRES SPREAD IN
THREE WAYS
DIRECT FLAME CONTACT
RADIANT HEAT
EMBERS
Notes: Talk through these three main causes using the next three slides and get the students to complete a labelled diagram of the three main causes in their learning journals.

## Slide 16
DIRECT FLAME CONTACT
Flames touch the unburnt fuels (leaves, twigs, bark, grasses) and raise their temperature. This causes the unburnt fuels to catch alight.

## Slide 17
2. RADIANT HEAT
Radiant heat is the heat produced by a fire. In a bushfire, the radiant heat can get so hot that it causes the temperature of unburnt fuels to increase enough for them to catch alight. This can happen before the flames touch the fuels.
Notes: Note: most lives are lost due to radiant heat. People caught out in the open or in cars perish due to radiant heat, before the flames get near them.

## Slide 18
3. Embers
Embers are burning leaves and twigs that are carried by the wind and start ‘spot fires’ where they land. If the spot fire is not put out, it can smoulder and spread. In strong wind, burning embers can travel many kilometers through the air and start spot fires when they land.

## Slide 19
Notes: Link: https://www.youtube.com/watch?v=p1iZPR6aIBc
Introduce the video: “This video of controlled burn shows how a fire can spread via direct flame contact, radiant heat and embers. The was fire was lit by bushfire scientists at the CFA and CSIRO to test how well the CFA fire trucks can stand up to radiant heat, ember attack and direct flame contact. There are no people in the firetrucks and the surrounding area had been burnt previously to stop the fire spreading out of control. The CFA also have a lot of firefighters and firefighting equipment to keep the fire within the containment lines. Although it is just a test, it does show you how quickly fire can spread, and you can see how it travels. As we watch the video, we will try to find examples of direct flame contact, radiant heat and embers.”
Key points in the video:
00:00 – 2:24 provides important background information about the test.
02:24 – 4:40 shows the fire spreading by direct flame contact
4:40 – 5:05 shows embers igniting spot fires ahead of the main fire front
5:05 shows a tree trunk igniting due to radiant heat (Notice that the flames have not touched the tree – the heat generated by the fire is intense enough to ignite the bark on the tree trunk).
6:29 shows the fire reaching a temperature of 720 degrees Celsius but the firetruck has been built to withstand these temperatures and it standing up well.
6:45 shows that the time since the fire started is only 4 minutes.
At these key points in the video, press pause to have a class discussion about how the fire is spreading.
At 06.45 you can stop the video and tell the students that the test was successful and that the firetrucks were able to stand up to direct flame contact, radiant heat and embers. The fire was extinguished by the CFA and everybody was safe. This is just one example of the hundreds of tests and experiments our Victorian that bushfire scientists have conducted to gain a better understanding of bushfire behaviour.
Give the students more time to finish their diagrams, label the describe the mechanism of fire spread under each one.

## Slide 20
BUSHFIRE BEHAVIOUR
BUSHFIRE BEHAVIOUR refers to how quickly a bushfire spreads, how much radiant heat it generates, and how much vegetation it burns.
Notes: RECAP. Present this slide and facilitate a discussion about the fire in the CFA video. Discussion prompts:
How did the fire start?
How did that fire spread?
How quickly did it spread?
How much radiant heat did it generate? (the temperature in the fire reached 720 degrees)
How much vegetation did it burn?

## Slide 21
Bushfire behaviour is influenced by three main factors:
FUEL
WEATHER
TOPOGRAPHY
Notes: Tell the students that bushfire behaviour is influence by four main factors: Facilitate a short discussion about these three factors:
What do we mean by fuel? How does fuel influence bushfire behaviour?
What do we mean weather? How does weather influence bushfire behaviour?
What do we mean by topography? How does topography influence bushfire behaviour?
Get the students to make a title page in their learning journals for Bushfire Behaviour. They can include the information on this slide.

## Slide 22
PART 4
FUEL

## Slide 23
Notes: Present the slide. Ask the students:
What vegetation type do you think this is? NOTE: Fire ecology recap - If they need clues get them to choose from forest, woodland, grassland, scrub, shrubland, etc). (Answer: Woodland)
Do you think there could be a bushfire in this place? Why? (Confirm that there is a lot of fuel for a bushfire).

## Slide 24
Bushfire fuel is mostly made up of leaves, twigs, bark, grasses, shrubs and fallen branches. They catch alight easily and burn quickly. They are the ‘fuel’ for the bushfire.
BARK
GRASSES
SHRUBS
LEAVES & TWIGS
FALLEN BRANCHES
Notes: Talk through the information on the slide, pointing out the different types of fuel.
Ask the students: Why do these things catch alight easily and burn quickly? (A: These fuels dry out fast and heat up quickly as a fire approaches, which means they catch alight and burn easily)

## Slide 25
A fuel assessment involves looking very carefully at four things:
  Fuel size
  Fuel moisture
  Fuel Arrangement
  Fuel quantity
When fire fighters are predicting how a bushfire will behave in the landscape, they do a fuel assessment.
Notes: Talk through the information on the slide. Tell the students they are going to learn about these four things and how they influence bushfire behavior.

## Slide 26
FINE FUELS
Grasses, leaves, bark and twigs that are less than 6mm diameter.
HEAVY FUELS
Fallen branches, logs and stumps
that are more than 6mm in diameter.
6mm
Heavy fuels take longer to catch alight, but once they are alight they burn for a long time. They also create more radiant heat and are harder to put out.
Fine fuels catch alight easily. They burn very quickly and feed the spread of the bushfire. When there are a lot of the fine fuels, a bushfire can spread through the landscape very quickly.
1. FUEL SIZE
Notes: Talk through the information on the slide. Facilitate a discussion about flammability of fine fuels versus heavy fuels. Suggested prompts:
Which fuels would catch alight first – the fine fuels or the heavy fuels? (A: Fine fuels)
Which fuels would burn quicker – the fine fuels or the heavy fuels? (A: Fine fuels)
Which fuels would burn for the longest amount of time - the fine fuels or the heavy fuels? (A: Heavy fuels)
Which fuels would create the most radiant heat – the fine fuels or the heavy fuels? (A: : Heavy fuels)
Which fuels would be harder to put out - the fine fuels or the heavy fuels? (A: : Heavy fuels)
Students make make a heading for Fuel Size in their learning journals. Create a labelled diagram for fine fuels and heavy fuels and include

## Slide 27: How would you build a campfire?
Which fuels would catch alight first?
Which fuels would burn fastest?
Which fuels would catch alight last?
Which fuels would burn the longest?
Which fuels would create the most radiant heat?
Would you be able to start a campfire without the fine fuels?

## Slide 28
FINE FUELS
Grasses, leaves, bark and twigs that are less than 6mm diameter.
HEAVY FUELS
Fallen branches, logs and stumps
that are more than 6mm in diameter.
6mm
Heavy fuels take longer to catch alight, but once they are alight they burn for a long time. They also create more radiant heat and are harder to put out.
Fine fuels catch alight easily. They burn quickly and feed the spread of the bushfire. When there are a lot of the fine fuels, a bushfire can rapidly spread through the landscape.
Notes: Students make make a heading for Fuel Size in their learning journals.
Students create a labelled diagram for fine fuels and heavy fuels and include an explanation of how they burn in a bushfire.

## Slide 29: FINE FUELS TREASURE HUNT
Organise yourselves into teams of two. Each team will be given four brown paper bags.
Your team needs go outside into the schoolyard and collect four DIFFERENT types of fine fuel from the ground:
        Grass
        Leaves
        Bark
        Twigs
Put each type of fine fuel in its own bag.
The first team to return to the classroom with the four different types of fine fuel wins!
Notes: Provide students with the instructions for the Fine Fuels Treasure Hunt.
Keep the fine fuel samples on hand for future reference and use.
Encourage the students to look for evidence fine fuels on their property, in their neighbourhood and around the local area and report back with their observations.

## Slide 30
2. Fuel moisture
What is ‘moisture’?
How does the amount of moisture in the fuel affect how it burns?
Notes: Facilitate a short discussion about fuel moisture. Discussion prompts:
What is ‘moisture’? (A: Moisture is a form of water vapour. Water Vapour is tiny invisible drops of water that make something ‘moist’)
How does the amount of moisture in the fuel affect how it burns?

## Slide 31
This is the same Victorian grassland photographed at different times of year.
August
December
February
Notes: Present the slide. Facilitate a discussion about the moisture consent in the grassland. Discussion prompts:
When is the moisture content in the grass highest? (A: August) Why would it be highest at this time? (A: This is during winter when the weather is cold and rainy)
When is the moisture content in the grass lowest? (A: February). Why would it be lowest at this time? (A: This is in late summer when the weather is hot and dry/no rain).
When would the grass be most flammable? (A: February) Why? (A: There is very little moisture in the grass so it will catch alight easily and burn quickly)

## Slide 32
How can we measure the moisture content in fine fuels?
Pick up some pieces of leaf litter from the top and bottom of the fuel bed and grind them up in your hand. Completely dry fuel will crumble and feel dry. If there is any moisture in the fuel it will leave your hand feeling a bit wet or dirty.
Walk on some dead fuels and listen to the crunch. Very dry fuel will have a distinct sound underfoot, like walking on cornflakes.
Notes: Talk through the first method on the slide. Take the students outside to find some leaf litter (NOTE: If there is not leaf litter in the school yard, collect some and make a pile in advance). Get the students to pick up some leaf litter from the top and the bottom of the pile and ground them up. Tell them that completely dry fuel will crumble. If there is moisture in the fuel it will leave your hand feeling a bit wet or dirty. OPTIONAL: If you have the appropriate safety requirements in place, you may want to demonstrate the influence of moisture content with a small test. Burn some leaves that are completely dried out and some leaves that are very moist.
Talk through the second method on the slide. Encourage the students to try this the next time they see a pile of dead fuels (NOTE: Piles of dry bark and leaves work best!)

## Slide 33
5. CANOPY: The tops of the trees
3. ELEVATED FUEL: Small shrubs and young trees
2. NEAR SURFACE FUEL: Small plants and grasses growing close to the ground
THE FIVE FUEL LAYERS
4. BARK FUEL: Bark on tree trunks and branches
3. FUEL ARRANGEMENT
1. SURFACE FUEL: Leaves, twigs, bark and other fine fuel lying on the ground
Notes: Talk through the different fuel layers. When you get to ‘4. Bark Fuel’, ask the students if they remember what happened with the bark fuel in the CFA test video (A: The bark ignited easily and carried the fire up into the canopy. It also created embers that started new spot fires away from the main fire front)
NB: This slide is animated. With each click a new fuel layer will appear.

## Slide 34
Notes: Display the image.
Invite a student to come and point out some surface fuels - Leaves, twigs, bark and other fine fuel lying on the ground). Ask students to recall the diameter of fine fuels (A: Less than 6mm).
Invite a student to come up and point out some near surface fuels (grasses, and small plants growing close to the ground).
Invite a student to come up and point out some elevated fuels (small shrubs and young trees)
Invite a student to come up and point out some bark fuel (bark on tree trunks and branches). Ask students to recall what happened with the bark fuel in the CFA test video (A: The flames and the radiant heat ignited the bark fuels which carried the fire up into the canopy)
Invite a student to come up and point out a canopy (the tops of the trees)

## Slide 35: FUEL LAYER TREASURE HUNT
Organise yourselves into groups of four.
Each group has a Treasure Hunt Map and Checklist.
Your job is to find an example of each fuel layer in the schoolyard.
When you find the fuel layer:
Tick it off the checklist
Write the name of the fuel layer on a sticker and place it on the correct location on the map.
You have 10 minutes. Go!
Notes: Provide each group with a print out of the Fuel Arrangement slide, as well as a Treasure Hunt Map (an A3 map of the schoolyard taken from google maps) and a Treasure Hunt Checklist (found here on the website: https://www.cfa.vic.gov.au/ArticleDocuments/2734/Bushfire%20fuels%20treasure%20hunt.docx).
Do a short demonstration of what the students are required to do before sending them out into the schoolyard (i.e.. write ‘surface fuels’ on a sticker, stick it on the map, and tick it off the checklist)

## Slide 36
What is a fuel ladder?
SURFACE FIRE
These fires burn the fine fuels close to the ground. In hot, dry, windy conditions they can get out of control very quickly.
1. A fire starts in the surface fuels.
2. The flames from the burning surface fuels ignite the near surface fuels.
3. The fire spreads up to elevated fuels and bark fuels. The flames get bigger and the radiant heat increases.
4. The flames and radiant heat from the elevated fuels and bark fuels ignite the canopy.
CROWN FIRE
These fires spread rapidly through the landscape, create intense radiant heat, and do significant damage to the tree.
Notes: NOTE: This slide is animated.
Display the slide. Ask the students to recall the CFA fire test video. Did that fire get up into the canopy? How did the fire get up into the canopy? (answer: it travelled up the bark)
Talk through the different levels of the fuel ladder. NB: This slide is animated so you can talk though each level of the fuel ladder and show how the fire climbs up.
Ask the students if they have ever seen a fuel ladder in their local area or while out in the bush? Encourage the students to keep an eye out for any fuel ladders in the local area and report back.

## Slide 37
Notes: This is a photo of a bushfire in Maui, Hawaii. Ask the students, ‘What is going on this photo?’ ‘Can you see the fuel ladder that is carrying the fire up into the tree canopy?’
Ask the class: If you could back in time to one day before this fire, what could you do to prevent the fire from getting up into the tree canopy? (A: Break the fuel ladder - remove the surface fuels, near surface fuels and elevated fuels from around the tree). Invite some students to come up and outline their ‘fuel management strategy’.

## Slide 38
4. FUEL QUANTITY
You CAN walk through in a straight line without vegetation blocking your way.
You CANNOT walk through in a straight line without vegetation blocking your way.
LOW FUEL QUANTITY
HIGH FUEL QUANTITY
Notes: Talk through the information on the slide. Ask the students to provide some examples of low fuel quantity and high fuel quantity in the local area.
NOTE: It can be fun to find local examples using streeview on google maps. For example, this street view from Monbulk Road in the Dandenongs shows a high fuel load.
https://www.google.com/maps/@-37.8179188,145.4069911,3a,75y,229.38h,90t/data=!3m7!1e1!3m5!1s0_h-C3msgjPA13nbiXTiNg!2e0!6shttps:%2F%2Fstreetviewpixels-pa.googleapis.com%2Fv1%2Fthumbnail%3Fcb_client%3Dmaps_sv.tactile%26w%3D900%26h%3D600%26pitch%3D0%26panoid%3D0_h-C3msgjPA13nbiXTiNg%26yaw%3D229.37566!7i16384!8i8192?entry=ttu&g_ep=EgoyMDI0MTIxMS4wIKXMDSoASAFQAw%3D%3D

## Slide 39: What would a bushfire be like with a low fuel quantity?
Low fuel
Low intensity fire
High intensity fire
Bonus question!
Is this a surface fire or a crown fire?
Notes: NOTE: This slide is animated.
Ask the students: “What would a bushfire be like with a low fuel quantity?” Get the students to stand up or sit down to indicate their answer. Show the answer with the animation.

## Slide 40: What would the fire intensity be like with an extreme fuel quantity?
Low intensity fire
High intensity fire
Extreme fuel
Bonus question!
Is this a surface fire or a crown fire?
Notes: NOTE: This slide is animated.
Ask the students: “What would a bushfire be like with a low fuel quantity?” Get the students to stand up or sit down to indicate their answer. Show the answer with the animation.
Facilitate a short discussion about fuel loads in the local area. Discussion prompts:
What’s the fuel quantity like in our school yard – low or extreme?
Can you think of any places in our local area with a low fuel load?
Can you think any other places in our local area with an extreme fuel load?

## Slide 41
PART 5
WEATHER

## Slide 42
How does the weather influence bushfire behaviour?
Notes: Facilitate a class discussion to elicit the students existing knowledge of the influence of weather on bushfire behaviour. Suggest discussion prompts:
How does weather influence bushfire behaviour?
What kind of weather would be the most dangerous for bushfires? Why?

## Slide 43
Notes: Play the video from 00:00 to 1.54. NOTE The second half of the video talks about fire danger ratings. This topic is covered in the next module (Module 5: Bushfire Risk).
When the video is finished, facilitate a discussion about the following key points. The timestamps for the relevant parts of the video are provided so you can all rewatch the video and check your answers.
00:34: When does the bushfire season peak in our local area? (A: December to February). Why do you think the bushfire season peaks during that time? (A: The weather is hotter and dryer and there is rain)
00:42 What weather conditions cause the vegetation to dry out and become more flammable? (A: hot temperatures, low humidity, low rainfall)
00:50 How does wet weather influence the amount the fuel? (A: It encourages vegetation growth, increasing the amount of fuel)
01:00 How does wind influence the fire behavior (e.g. wind fans the flames and cause a fire to spread faster; strong winds can carry hot embers long distances which can start spot fires many kilometers ahead of the main front; a change in wind direction can shift the direction of the fire, altering the course of the fire and broadening the fire front)

## Slide 44
RAIN
HUMIDITY
TEMPERATURE
WIND
Temperature influences the amount of moisture content in fuel.
As the temperature increases, the moisture content in the fuel decreases and it catches alight more easily.
Higher temperatures also heat up the fine fuels, so they catch alight more easily.
In high humidity, the air feels damp and muggy. High humidity increases the moisture content in the fine fuels, so they don’t catch alight easily.
In low humidity the air feels dry. Low humidity reduces the moisture content in the fine fuels, so they catch alight easily.
Periods of rain encourage vegetation growth which increases the amount of fuel.
A lack of rain dries out the fuel, so it catches alight more easily.
Periods of drought can lead to very dangerous bushfire behaviour because there is no moisture in the fuel.
Strong winds fan the flames and push the fire through the landscape.
Strong winds carry embers through the air, starting new fires many kilometers ahead of the main fire.
A change in wind direction can push the fire in another direction and increase the size of the fire front.
1.
2.
3.
4.
Notes: Facilitate a discussion about the influence of temperature, rain and humidity on bushfire behaviour using the information on the slide as a guide. Suggested discussion prompts:
How does temperature influence fire behaviour?
How does humidity influence fire behaviour?
How does rain influence fire behaviour?
How does wind influence fire behaviour?

## Slide 45
Notes: Provide each student with a lessons from the past worksheet (https://www.cfa.vic.gov.au/ArticleDocuments/2734/Worksheet%203_Lessons%20from%20the%20past.docx) or instruct them to copy this table into their learning journals.

## Slide 46
Notes: Video link https://youtu.be/zCgBos3evdk
NB: This is a modified version of this video and isn't public. The public version contains distressing footage of injured and deceased wildlife and is not appropriate for children.
Play the first segment about the 1939 Black Friday bushfires 00:00 - 02:16. Facilitate a discussion about the weather conditions on Black Friday. Instruct the students to enter any information they may have missed. In the notes below, you will find some additional details to share with the students that they can enter into their table. Discussion prompts:
Had there been much rainfall in the years leading up to Black Friday? (A: No, there had been years of drought)
What was the temperature on Black Friday? (A: Temperatures soared above 40 degrees. NOTE: According to other sources, the temperature in Melbourne was 44.7 degrees).
What was the wind like Black Friday? (A. Dry northerly winds swept across Victoria. The wind had great force. NOTE: Northerly winds come from Central Australia and in the summer, these winds are very hot. According to other sources, the wind was gusting up to 60km per hour)
Did the video say anything about the level humidity? (A. No. NOTE: According to other sources, the humidity was very low – probably below 15%)
Play the second segment about the Ash Wednesday fires in Victoria 02:16 – 04:53. Facilitate a discussion about the weather conditions on Ash Wednesday. In the notes below, you will find some additional details to share with the students that they can enter into their table. Discussion prompts:
What was the temperature like on Ash Wednesday? (A: It was scorching hot. NOTE: according to other sources, the temperature in Melbourne was 43 degrees).
Had there been much rain in the leadup to Ash Wednesday? (A: No, there has been a short but intense drought)
What do think the humidity was like on Ash Wednesday? (NOTE: The video doesn't mention humidity but according to other sources, it was below 15%).
What was the wind like on Ash Wednesday? (A: Fierce winds Wind gusts of up to 100km/hr. There was a south westerly wind change just before nightfall)
Play the third segment about the Black Saturday bushfires 02:47 onwards. Facilitate a discussion about the weather conditions on Ash Wednesday. In the notes below, you will find some additional details to share with the students that they enter into their table. Discussion prompts:
What was the temperature like on Black Saturday (A: Very high. NOTE: According to other sources, temperatures in Victoria reached 46.4°C)
Had there been much rain in the lead up to Ash Wednesday? (A: No, there had been 12 years of drought).
What do you think the humidity was like on Black Saturday (NOTE: The video doesn't mention humidity, but according to other sources humidity was less than 2%).
What was the wind like on Black Saturday? (A : Strong northwesterly winds pushed hot air in from the desert. NOTE: According to other sources, wind speeds reached 100km/hr)

## Slide 47
We are going to go outside and estimate the temperature, humidity, rainfall since 9am and the wind speed and direction.
You will need to bring your FEELING THE WEATHER worksheet and a pen
or pencil.
Notes: Provide each student with a feeling the weather worksheet ( https://www.cfa.vic.gov.au/ArticleDocuments/2734/Worksheet%204_Feeling%20the%20weather.docx.aspx ).
Take the students outside. Ask them to close their eyes for and tune into the current weather conditions:
Temperature – is it cold, warm, hot?
Humidity - does the air feel damp or dry?
Rain - has it today?
Wind speed –is there any wind? Is it a strong wind or a light wind? Which direction is it coming from?
Tell the students to open their eyes again. Ask them to:
Estimate the current temperature and record it on their sheet
Estimate the humidity level and record it on their sheet
Estimate the amount of rain since 9 am and record it on their sheet
Estimate the wind speed and direction and record it on their sheet
Return to the classroom.

## Slide 48
Open your laptop
Open google
Enter search words
BOM Weather and the name of
your town or suburb
Check your estimates!

## Slide 49
How would a bushfire behave in today’s weather conditions?
Temperature
Humidity
Rainfall
Wind
Notes: Facilitate a discussion about how a bushfire would behave in the current weather conditions. Discussion prompts:
  If a fire started in our local area today, would the fuel catch alight easily? Why/Why not?
  If a fire started in our local area today, would it spread quickly? Why/Why not?
Facilitate a discussion about the local weather conditions during peak bushfire season. Discussion prompts:
  When is peak bushfire season in our local area?
  What are the weather conditions like during that time?
  What does this mean for bushfire safety in our community?

## Slide 50
QUIZ TIME!
Notes: Link to Kahoot quiz https://create.kahoot.it/share/bushfire-behaviour-in-the-landscape-weather/079482cc-c2b4-4f4d-a4be-6a28e1484f82
Upon completion of the quiz, facilitate a discussion about the value and importance of what they have learned. Discussion prompts:
How important is it for people to understand the influence of weather on fire behaviour? Why? Emphasise that knowledge is power – if you know that the weather is going to be bad for bushfires, you can get prepared and make good decisions about your own safety. You can also educate other people so that they can get prepared and make good decisions too.
Do you think everyone in our community understands the influence of weather on fire behaviour? Emphasise that a lot of people don’t understand the influence of weather on fire behaviour. On a hot, dry, windy day with low humidity, they don’t think about the possibility of a bad bushfires because they haven’t learned about it like you have.
What could we do to help educate our community about the influence of weather on fire behaviour? Encourage the students to come up with as many ideas as they can (e.g. tell people about it, make a video and put it on social media, write an article for the school newsletter, do a presentation at school assembly.

## Slide 51
BE BUSHFIRE WEATHER WISE
THE PROBLEM
Some people don’t understand the influence of weather on fire behaviour. This means that on a hot, dry, windy day with low humidity, they don’t think about the possibility of bushfires and they don’t take the necessary precautions.
YOUR TASK
Create a poster that teaches people about the influence of weather on fire behaviour. It must include information about temperature, humidity, rainfall and wind. Use text and images to make it eye catching and engaging. Be creative, but stick to the facts!
Notes: OPTIONAL ACTIVITY
Your task is to design a poster to educate our community about the influence of weather on fire behaviour. It must include information about the influence of temperature, humidity, rainfall, and wind. Make it eye catching and engaging. Be creative, but stick to facts. Your goal is to clearly communicate the influence of weather on fire behaviour.

## Slide 52
PART 6
TOPOGRAPHY

## Slide 53
WHAT IS TOPOGRAPHY?

## Slide 54
Topography is the ‘lay of the land’. It describes the physical features of an area of land. These features include natural formations, such as hills, mountains, valleys, rivers, lakes and plains.
Do we have any of these natural formations in our local area?
How might these natural formations influence bushfire behaviour?
Notes: Source: https://gisgeography.com/what-is-topography/
Talk through the information on the slide.
NOTE: When discussing the influence of rivers and lakes, make sure the students understand that these landforms will not necessarily stop a bushfire because embers can travel from one side to the other.

## Slide 55
The influence of slope
A fire will burn faster up a slope. This is because the flames can easily reach more unburnt fuel in front of the fire. Radiant heat pre-heats the fuel in front of the fire, making the fuel even more flammable. For every 10˚ slope, the fire will double its speed.
For every 10° of uphill slope, double the rate of spread
5km/h
10km/h
Notes: Talk through the information on the slide.
NOTE: It is important to emphasise that for every 10 degrees of uphill slope you need to double the speed. For example, if the fire speed is 5km/hr on flat ground and the uphill slope is 20 degrees you need to double 5km/hr (which is 10km/hr) and then double it again (which is 20km/hr).

## Slide 56
For every 10° of downhill slope, halve the rate of spread
Fire travels slower downhill because there is more space between the flames and the new fuel to burn.
5km/h
2.5km/h
Notes: Talk through the information the slide.
NOTE: It is important to emphasise that for every 10 degrees of downhill slope you need to halve the speed. For example, if the fire speed is 5km/hr on flat ground and the downhill slope is 20 degrees you need to halve 5km/hr (which is 2.5km/hr) and then halve it again (which is 1.25km/hr).

## Slide 57
10° uphill slope
10km/h
20° uphill slope
10km/h
?
?
CAN YOU PREDICT THE RATE OF SPREAD?
For every for every 10° of uphill slope, double the rate of spread
Notes: The answers are on the next slide

## Slide 58
10° uphill slope
10km/h
20° uphill slope
10km/h
20km/h
40km/h
ANSWERS
For every for every 10° of uphill slope, double the rate of spread

## Slide 59
20km/h
20° downhill slope
20km/h
?
?
CAN YOU PREDICT THE RATE OF SPREAD?
For every for every 10° of downhill slope, halve the rate of spread
10° downhill slope
Notes: The answers are on the next slide.

## Slide 60
20km/h
20° downhill slope
20km/h
10km/h
5km/h
ANSWERS
For every for every 10° of downhill slope, halve the rate of spread
10° downhill slope
Notes: Answers

## Slide 61
PART 7
WHAT HAVE WE LEARNED ABOUT BUSHFIRE BEHAVIOUR?

## Slide 62
QUIZ TIME!
Notes: Do the Kahoot quiz
https://create.kahoot.it/share/bushfire-behaviour-in-the-landscape/e1a866e7-b8a0-4f3a-8b5d-f9a359d22657

## Slide 63
END OF MODULE